## Slide 1: Modelling buildings and their heating systems
André Osthövener, Laura Brunn, Lita Ndaba
Tutor: Thilo Hartleif
Notes: Source picture: https://www.freepik.com/free-photos-vectors/renewable-energy-city
Alternative:
https://www.re-thinkingthefuture.com/architects-lounge/a334-5-renewable-energy-sources-that-are-going-to-impact-the-building-industry-in-the-future/

## Slide 2: Motivation for this topic
Goal: climate neutral buildings until 2045
residential buildings are responsible for 30% of greenhouse gas emissions
building energy act came into force on 1. january 2024 and ensures the switch to renewable energy for heating
different paths to archieve climate-neutral houses
→ our task is to analyse some of them
Notes: Facts from DENA Gebäudereport 2024
part of heat transition is to renovate houses and use new technical building equipment
different paths to archieve climate-neutral houses
our task is to analyse some of them
goal: climate neutrality until 2045
residential buildings are responsible for 30% of greenhouse gas emissions
building energy act came into force on 1. january 2024 and ensures the switch to renewable energy for heating and hot water
2022: 19,5 million residential buildings, 13 million are single-familiy houses

## Slide 3: Motivation
In this course, we have mostly focused on electricity from renewable sources
Since we know how to make electricity (the most versatile energy carrier) without carbon emissions:
 transport and heating / cooling need to be electrified
Energy consumption in Germany in 2022 by electricity, heating, and transport

## Slide 4: Introduction – overview building stock Germany

## Slide 5: Building stock in Germany
Evolution of energy standards
Overview buildings stock
Overview heating systems
Chosen houses for the scenarios

## Slide 6: Building stock in Germany - energy standards
1973 | EnEG: Energy Saving Act regulates energy use in buildings
1977 | WSchV: first Thermal Insulation Ordinance regulating heat insulation of buildings
1978 | HeizAnlV: Heating System Ordinance regulating design and efficiency of heating systems
2002 | EnEV: Energy Saving Ordinance, introduced primary energy demand and U-values as key criteria
2009 | EEWärmeG: Renewable Energies Heat Act, requires use of renewable energies in new buildings
2020 | GEG: Building Energy Act, regulates energy use and renewable integration integration in buildings
Notes: 1973 EnEG enacted in response to oil crisis, regulates energy use in buildings
1977 WSchV: first Thermal Insulation Ordinance regulating heat insulation of buildings
1978 HeizAnlV: Heating System Ordinance regulating design and efficiency of heating systems
2002 EnEV: Energy Saving Ordinance, merged WSchV and HeizAnlV, introduced primary energy demand and U-values as key criteria, several revisions
2009 EEWärmeG: Renewable Energies Heat Act, Germany‘s implementation of the EU Renwable Energy Directive, requires use of renewable energies in new buildings
2020 GEG: Building Energy Act, unifies EnEV, EEWärmeG, EnEG into single law regulating energy use and renewable integration integration in buildings

## Slide 7: Building stock in Germany – overview buildings
buildings by year of construction in per cent
Chart: year of construction
| before 1946 | 1946-1977 | 1978 - 2014 | after 2014
Verkauf | 25 | 35 | 35 | 5
Notes: Source: DENA Gebäudereport
roughly 25% of residential building were built before 1946 and 35% between 1946-1977
since the introductions of EnEV 2014 around 1 million = 5% of the residential buildings were built
nearly half of the housing stock are three- and four-room flats

## Slide 8: Building stock in Germany – overview buildings
2022: average flat size in new buildings
154 m2
112 m2
Trend since 2000:
76 m2
Average per capita living space:
1990:
34.8 m2
2022:
47.4 m2
Notes: Source: DENA Gebäudereport
nearly half of the housing stock are three- and four-room flats
In 2022, the average flat size in new builds was around 154 m^2 for detached houses and 112 m^2 for semi-detached houses. There has been a trend towards an increase in the size of detached and semi-detached houses since 2000. This trend can also be applied to room sizes
In multi-family houses, on the other hand, the size decreases and, at around 76 m^2, is generally smaller than that of the other types of flat
Average per capita living space has risen almost steadily since 1990 (34.8 m^2) and was around 47.4 m^2 in 2022

## Slide 9: Building stock in Germany – overview heating
proportion of residential units heated by heat pumps has been rising steadily since 2003, BUT: reaching 3% of all buildings in 2022
Coal
Oil
Gas
Elec-tricity
District h.
Heat pumps
Solar
Biomass and other
Completed buildings by energy type in per cent
Notes: Source: DENA Gebäudereport
from 2000 to 2022, the proportion of completed residential buildings with heat pumps as an energy source increased from almost 0% to 57%.
7,3 % were air-to-water heat pumps, brine-to.water heat pumps, water-to-water heat pumps and hot water heat pumps
proportion of residential units heated by heat pumpps has been rising steadily since 2003, reaching 3% in 2022

## Slide 10: Building stock in Germany – overview heating
2022 heating based on renewable energy in 22% of the general housing stock
heat consumption per heated square metre decreases annually due to climate change
the largest areas of application for energy consumtion in residential buildings are space heating (66%) and hot water (16%)
Notes: Source: DENA Gebäudereport
2022 heating based on renewable energy in 22% of the general housing stock
heat consumption per heated square metre decreases annually due to climate change
the largest areas of application for energy consumtion in residential buildings are space heating (66%) and hot water (16%)

## Slide 11: Building stock in Germany – chosen houses
Based on information before, we choose these 3 houses:
25% before 1946 → Tabula data for 1919 - 1948
35% before 1977 → Tabula data for 1958 - 1968
a modern one → Tabula data for 2016
The heating season in Germany is 200 days per year
Notes: (https://s2.building-typology.eu/abpdf/DE_N_01_EPISCOPE_CaseStudy_TABULA_National.pdf)

## Slide 12: Introduction – heat pump

## Slide 13: How does a heat pump work - principle

## Slide 14: How does a heat pump work?
AC v Heat pump
COP with some heat flow math

## Slide 15: Coefficient of Performance (COP)
What is COP
The Coefficient of Performance (COP) is a measure of the effectiveness of heat pumps, refrigerators, and air conditioners. It indicates how efficiently a system transfers heat relative to the amount of work it consumes.
where:
QH is the heat delivered by the heat pump
Win is the work input to the system
Kcooling = is the cooling coeffcient

## Slide 16: How do different heat pumps work? ASHP vs. GSHP
feature | ASHP | GSHP
heat source | air | ground
heat absorption | air that is blown over the heat exchanger by a fan → usually comprise a single, self-contained outdoor unit | by refrigerant running through a series of buried pipes → can be laid horizontally and buried in trenches just over a metre deep → can also be laid vertically in boreholes a single pipe loop might need around 600 m^2, larger buildings may require a second loop a single pipe loop might need around 600 m^2, larger buildings may require a second loop (/ open loop system that directly extracts heat from a pond or other source of water)
cost | not that expensive | expensive
temperature stability | varies with weather | relatively stable around the year
efficiency | lower in cold climates | generally higher, especially in winter
Notes: Source: https://www.granddesignsmagazine.com/heating/air-source-heat-pumps-vs-ground-source-heat-pumps/

## Slide 17: How does a heat pump work? -> COP and what influences it
What are the main parameters that influence the COP of heat pumps?
COP = generated heating energy (kWh) / electricity consumed to generate heat (kWh)
source temperature, sink temperature
system design like control devices, compressor, type of refrigerant, length and dimension of piping, sizing of heat exchangers
higher COPs are associated with longer cycle times required for more complete desorption and adsorption processes, resulting in a lower number of cycles per unit time and consequently in lower specific heating or cooling power
How do ASHP and GSHP differ in this context?
GSHP are more efficient, roughly: COP=6, ASHP COP=4
Notes: https://gebwell.fi/en/news/how-is-the-cop-of-a-heat-pump-calculated-and-what-affects-it/ ;
Vítor A.F. Costa, João M.S. Dias, On the best coefficient of performance and specific heating or cooling power combination for adsorption refrigerators and heat pumps, International Journal of Refrigeration
2023

## Slide 18: our model

## Slide 19: What‘s Modelica
What are the main principles?
object-oriented, equation based, declarative modeling language
designed to model complex physical systems involving multiple physical domains like mechanical, electrical, thermal

## Slide 20: What‘s Modelica
What are main differences to other modelling tools?
Uses equations to describe relationships rather than commands
Components can easily be reused in different configurations
Several pre-built components for physical modeling
Has symbols to represent the physical model
Notes: And we added the window manually

## Slide 21: What‘s Modelica - AixLib
is a library designed for modeling and simulating building energy systems
based on IBPSA library (International Building Performance Simulation Association)
provides models for
  Heating, Cooling,
  Ventilation Systems
  Building Envelope
  Control Strategies
  Weather Data Handling

## Slide 22: Weather data (2015)
TRY makes lots of data available
Maybe show the uploaded video animation of weather data in Germany

## Slide 23: Assume ground temperature as constant
Tabula heating days:

## Slide 24: Preprocessing
Choose weather file
Choose building file
Modelica‘s “dassl“ integratior actually adapts the step size
It takes >10 minutes to run a full year
Custom Python script to reformat temperature data
Write custom files with all building parameters
Before Simulation

## Slide 25: Modelica Simulation Run

## Slide 26: Parameters
Tabula website with building stock data across Europe
Validate the model by checking if results can be reproduced with real data
No ventilation, no internal heat source, no solar irradiance
https://webtool.building-typology.eu/?c=de#vares

## Slide 27: Tabula parameters
Tabula provides the surface area and thermal transmittance (U) of the components: floor, walls, windows, roof
For the model, we also need the volume of air inside

## Slide 28: Validating the model with Tabula
Tabula provides information about heat losses of real houses
Heat loss Q per area equals energy loss E during heating season (200 days) per floor area in [kWh/m2a]:

## Slide 29: Validating the model with Tabula – example
Typical building explain plots here??

## Slide 30: Comparisons (relevant plots)
Controller
Misc
Heat pump
Building

## Slide 31: How are different types of building performing?

## Slide 32: 1978 typical building in 2015 weather
Heat pump fails to meet room set temperature
Only when ambient T is >20°C, so is T inside
Even though the control valve is fully opened
And although the COP during the heating period was 4.5 on average

## Slide 33: 1978 refurbished building
Tabula claims Our results
Our model does not account for ventilation
Error potentially explained by different weather data, location, etc.
Interpretation of our bars:
All energy that was put into the house (gains) must be lost as well (so bars must be same height)
All gains came from the sum of electrical energy for the HP and heat energy from the borehole. „Blue moved orange“

## Slide 34: 1978 refurbished vs 2016 building
Refurbishing a 1978 building gets it very close to 2016 performance
Many non-linearities, but as a rough estimate: sum of U-values is 20% less for 2016 building, and it‘s losses (and therefore energy demand) is about 17% less

## Slide 35: 2016 building in normal vs cold winter
Total electricity demand: 2322 kWh
vs 2513 kWh in the cold winter.
Both reasonably close to tabula results
Interesting that the window T changes so much. If that figure stays I need to update the colors to match

## Slide 36: 1948 refurbished building in 2015
But that needed HP=2 and
T_HC_1_amb=273.15-20, T_HC_1_sup=273.15+70, T_HC_2_amb=273.15+20, T_HC_2_sup=273.15+20
T_HC_1_amb=273.15-20, T_HC_1_sup=273.15+70, T_HC_2_amb=273.15+20, T_HC_2_sup=273.15+20

## Slide 37: Different housing types - conclusion

## Slide 38: What does a night setback change?

## Slide 39: Night setback difference 2015 normal
„old“ building 1978
„new“ building 2016

## Slide 40: Night setback - conclusion

## Slide 41: How will buildings perform in future weather scenarios?

## Slide 42: 2016 house 2015 and 2045 weather compared
What is the difference between winter 2015 and 2045?
Notes: Jan-Apr

## Slide 43: 2016 house 2015 and 2045 weather compared
2015
49.8 kWh/m2a
2172.7 kWh in heating period
Notes: Jan-Apr

## Slide 44: 2016 house 2015 and 2045 weather compared
2045
43.63 kWh/m2a
1839.3 kWh in heating period
2015
49.8 kWh/m2a
2172.7 kWh in heating period
Notes: Jan-Apr

## Slide 45: 2016 house 2045 normal weather and cold winter compared
What is the difference between a normal and a cold winter?

## Slide 46: 2016 house 2045 normal weather and cold winter compared
2045
43.63 kWh/m2a
1839.3 kWh in heating period
2045
51.9 kWh/m2a
2380 kWh in heating period

## Slide 47: Future weather - conclusion
Normal weather 2045 and 2015 are not that different
Cold winter 2045: the few very cold days lead to more loss
To prevent loss: most loss window and wall -> better isolation of window and wall in future houses

## Slide 48: Conclusions I
Most losses: [compare losses different scenarios]
-> renovate walls, windows, …
Right now, only 3% of buildings in Germany are renovated (2024)
Notes: 3% fact: Frauenhofer Institut, Pressemitteilung Mai 2024

## Slide 49: Is it realistic to renovate all old buildings?
Renovation is expensive, is it economical?
Federal funding for efficient buildings:
  Heating system: up to 70% of cost
  Other efficiency meassures like insulation, windows, ventilation system: up to 20% or 30.000 €
  Loans with low interest rates for efficiency meassures
Notes: Federal funding:
https://www.energiewechsel.de/KAENEF/Redaktion/DE/Dossier/beg.html?etcc_cmp=energiewechsel&etcc_med=sea&etcc_par=google-ads&etcc_ctv=mdaemmbeg&etcc_bky=förderung%20fassadendämmung&gad_source=1&gad_campaignid=20016865430&gbraid=0AAAAACfZxDiOPDNiKPyyG1CXicbN_26UH&gclid=Cj0KCQjw64jDBhDXARIsABkk8J5f3hOwqKjqKJzkZljxGFYtAu1fWFUsPgu23k7WnnaC_GqcT5LiDHwaAk8SEALw_wcB

## Slide 50: Conclusions II
Most losses: [compare losses different scenarios]
Heating pumps make sense if house is well insulated
We [can / cannot] reduce losses with night set back
Notes: 3% fact: Frauenhofer Institut, Pressemitteilung Mai 2024

## Slide 51: Whats next?
Try different heat pumps

## Slide 52: Thanks for listening!

## Slide 53: Sources
Krähenmann, S., Walter, A., Brienen, S., Imbery, F., Matzarakis, A.: Stündliche Raster der Lufttemperatur für Deutschland (Projekt TRY-Weiterentwicklung), Version V001, DWD Climate Data Center (CDC), DOI:10.5676/DWD_CDC/TRY_Basis_v001, 2016

## Slide 54: 3 questions, 4 answers each
Which building type did we not simulate?
  1948
  1977
  2030
  2016

## Slide 55: Do you have any questions?

## Slide 56: Backup slides